## Slide 1
NETWORK ENGINEERING • ESPORTS PERFORMANCE
How Would You Optimize a
Network for Online Gaming?
A practical look at latency, bandwidth, hardware, and configuration
choices that keep competitive play smooth and lag-free.
S. KARTHIKEYAN
Reg. No: 192419048
01

## Slide 2
INTRODUCTION
Why Network Optimization Matters
In online gaming, the network sits between a player's input and the game server's response. Even small delays or drops in that path show up directly as rubber-banding, missed shots, and desync — regardless of how powerful the gaming PC is.
Optimization means treating the connection itself as part of the gaming rig — tuning it end to end, from the router in the room to the server region across the internet.
< 30 ms
Ping considered
ideal for FPS titles
3–5 Mbps
Bandwidth typically
needed per game session
0 ms
Target jitter for
stable, predictable play
02

## Slide 3
CORE FACTOR 01
Reduce Latency (Ping)
Latency is the round-trip time between a player's action and the server's acknowledgement. It is the single most noticeable factor in competitive, fast-paced games.
Wired over wireless
Ethernet removes Wi-Fi contention and radio interference that add unpredictable delay.
Nearest server region
Choosing a geographically closer server region cuts the physical distance data must travel.
Traffic prioritization
QoS rules on the router keep game packets ahead of downloads and streaming traffic.
Trim background load
Closing bandwidth-heavy background apps prevents queuing delay on the same link.
03

## Slide 4
CORE FACTOR 02
Manage Bandwidth Properly
Most games need surprisingly little bandwidth to run smoothly — the real risk is other devices on the same network saturating the link during play.
Competitive FPS / MOBA
~3–5 Mbps
4K game streaming (viewer)
~15–25 Mbps
Cloud game download / patch
Uses all available
Why it stalls
Shared connections choke when uploads/downloads compete for the same limited pipe, causing spikes in ping rather than a drop in raw speed.
04

## Slide 5
CORE FACTOR 03
Control Jitter & Packet Loss
Even with low average ping, an unstable connection causes visible stutter. Jitter is the variation in delay between packets; packet loss forces the game to resend or guess missing data.
Jitter
Caused by congested Wi-Fi channels or overloaded routers
Shows up as sudden rubber-banding after a smooth stretch
Reduced with QoS, a wired link, and a stable channel
Packet Loss
Often from damaged cables, weak Wi-Fi signal, or ISP congestion
Feels like input not registering or enemies teleporting
Reduced by fixing physical connections and updating firmware
05

## Slide 6
OPTIMIZATION STEP 01
Hardware & Physical Setup
01
Use a wired Ethernet connection
Direct cable to the router avoids Wi-Fi interference entirely — the single biggest upgrade for most home setups.
02
Position the router centrally
If Wi-Fi is unavoidable, place the router in an open, central spot away from walls, metal, and appliances.
03
Upgrade router & firmware
Modern routers support better QoS and Wi-Fi standards; keep firmware updated for stability fixes.
04
Limit connected devices
Fewer devices sharing the network during play means less contention for the same bandwidth.
06

## Slide 7
OPTIMIZATION STEP 02
Configure the Router (QoS)
Quality of Service (QoS) lets a router decide which traffic gets priority when the connection is busy — keeping small, time-sensitive game packets moving ahead of large downloads.
Enable QoS / Gaming Mode and prioritize the gaming device's IP or MAC address
Set the correct WAN bandwidth values so QoS calculates priority accurately
Disable unnecessary UPnP or open only the ports the game requires
Reserve a static local IP for the gaming console or PC to keep rules consistent
Traffic Priority Stack
Gaming Traffic
Voice / Video Calls
Web Browsing
Downloads & Updates
Higher priority reserved for real-time, low-tolerance traffic
07

## Slide 8
OPTIMIZATION STEP 03
DNS, Server & Route Selection
Switch to a fast DNS resolver
A responsive DNS service speeds up the initial connection and matchmaking lookups.
Manually select server region
Where the game allows it, pick the closest data center instead of relying on auto-selection.
Check the route with traceroute
Identify which network hop is adding delay before blaming the game itself.
Use a gaming VPN only if needed
A well-routed VPN can sometimes bypass ISP congestion, but adds a hop — test before committing.
08

## Slide 9
SUMMARY
A Quick Optimization Checklist
✓
Connect via Ethernet whenever possible
✓
Enable QoS and prioritize the gaming device
✓
Pick the nearest available server region
✓
Keep router firmware and drivers up to date
✓
Limit other devices' bandwidth use during play
✓
Test with ping, jitter, and packet-loss tools regularly
A well-tuned network turns raw hardware performance into consistent, responsive gameplay — the goal is a connection that behaves the same way every round.
S. Karthikeyan • Reg. No: 192419048
09